## Slide 1
Exact and Structural Methods for the
Job Sequencing and Tool Switching Problem
Mid-term results: a worst-case theory of the standard heuristic,
and what the benchmark campaign revealed about exact methods
Shankar Narayanan · advisors: Dr. R. Colares, Prof. A. Wagler · supervisor: Dr. R. Chicoisne
Notes: 30-second version: a CNC machine holds b tools; jobs need tool sets; reordering jobs changes how many tool swaps you pay. Everyone in practice groups jobs first, then sequences the groups. We built the first worst-case theory of that heuristic, and we benchmarked every exact method, including two of our own. Three headlines: (1) tight quantitative laws for the heuristic error, including refuting our own conjecture with a certificate; (2) the ratio bound 4/3 is now a theorem for K*<=3; (3) all exact methods live or die by one number, |U|-b, and the benchmark shows the instance families split about half and half on it.

## Slide 2
The problem in one picture
One machine, a small tool magazine, and an order to choose
CNC machine
tool 1
tool 2
tool 3
free
magazine: capacity b (here 4)
Each job j needs a tool set Tⱼ. A tool swap = remove one, insert one. Choose the job ORDER and the loading policy to minimise total insertions.
Known: for a FIXED order, optimal loading is easy — the KTNS rule (keep tools needed soonest), 1988.
Hard: choosing the order. The joint problem is NP-hard.
What practice does: group, then sequence
1
Group jobs so each group’s tools fit the magazine (JGP) — fewest groups
2
Order the groups like a small travelling-salesman tour (GSP)
3
Run KTNS on the flattened order
Used in industry (colour printing = this exact problem). Reported to work well — but nobody had analysed how badly it CAN fail.
SSP mid-term — 2
Notes: Terms to be comfortable with: magazine = tool holder of capacity b. T_j = tools job j needs. A switch/insertion is the unit of cost. KTNS = keep-tool-needed-soonest, the provably optimal eviction rule once the order is fixed (like optimal cache eviction). JGP = job grouping problem (pack jobs into fewest magazine-fitting groups; NP-hard but well solved). GSP = ordering the groups. The decomposition is the industry standard; Burger et al. 2015 applied it verbatim to colour printing and measured it empirically good. Our first question: how bad can it be in the worst case? Nobody had asked.

## Slide 3
Two questions, one number
The whole project hangs on the coverage bound
Q1 — the heuristic
How far can group-then-sequence be from the true optimum? When is it exact?
Q2 — exact methods
Can the SSP be solved exactly through tool configurations (column generation, Benders), the way JGP can?
|U| − b
used tools beyond the magazine = a lower bound every schedule must pay.
It is the LP value of every natural configuration relaxation (proved) — and, on many instances, the exact optimum.
Where it is tight: the heuristic tends to be exact AND exact methods finish at the root. Where it is loose: both struggle.
SSP mid-term — 3
Notes: |U| is the set of tools any job uses; b the capacity. Every tool outside the initial load must enter at least once: that is the coverage bound. Big picture to say out loud: the same quantity controls BOTH questions. That is the report’s thesis and the campaign measured it: about half the standard benchmark instances have optimum exactly equal to this bound.

## Slide 4
The smallest counterexample: the 6-ring
Six jobs on a cycle, b = 3 — the heuristic provably loses
j1
j2
j3
j4
j5
j6
jobs = edges of a 6-cycle: Tⱼ = {j, j+1}; adjacent jobs share one tool
Best possible (optimal): 3 switches — uses FOUR groups, each transition changes one tool
Heuristic (3 groups, best order): 4 switches
gap = 1, ratio = 4/3
The failure is the GROUPING phase: insisting on the fewest groups (K* = 3) hides the cheaper 4-group route. Replicating the ring g times makes the gap g — unbounded.
SSP mid-term — 4
Notes: Walk through slowly: costs are counted after a free initial load (free-initial convention). The optimum keeps tool 1 resident the whole time and pays 3. The heuristic must use 3 groups; any two of its 3 configurations differ in 2 tools, so it pays 4. Gap exactly 1 — certified. Say: this instance is our fruit-fly; it recurs in every result. And disjoint copies stack the gap, so no constant additive guarantee exists.

## Slide 5
What we proved about the heuristic (I)
The gap has an exact meaning — and exact off-switches
Exactness theorem. SSP optimum = cheapest walk over ALL groupings. So the heuristic’s gap is precisely the price of demanding the MINIMUM number of groups.
K* ≤ 2
zero gap, any b
|U| ≤ b+1
zero gap, any b
Z* ≤ 2
zero gap, any b
setup cost ρ > gap
heuristic exact
Practical collapse: with a per-changeover setup cost ρ (real machining: ρ ≈ 3–60), the heuristic becomes EXACTLY optimal — a rigorous licence for what practitioners already do.
SSP mid-term — 5
Notes: The exactness theorem is the conceptual reframe: grouping is not an approximation device, it is an exact lens; only the cardinality restriction costs anything. The four cards are proved zero-gap classes: few groups, few excess tools, tiny optimum, or any realistic setup cost. The last one matters for industry: if a magazine changeover has a fixed cost about equal to one switch or more, grouping-first is provably optimal.

## Slide 6
What we proved about the heuristic (II)
From a coarse guarantee to tight quantitative laws
At K* = 3, the heuristic cost in closed form:
H = q + min |(Cₐ ∩ Cᶜ) \ Cᵇ|
(q = |U| − b; minimum over 3-groupings and orderings — the middle configuration “shields” the overlap)
gap ≤ max(0, min(q, ⌊(2b−q)/3⌋) − R)
tight at EVERY known extremal instance
For every K*:
H/Z* ≤ min(b, K*−1, |U|−b)
gap ≤ ⌊q·(b(K*−1)−q)/(b+q)⌋ − R
(a probabilistic argument: order the groups at random, count how often each tool re-enters — Jensen does the rest)
4/3 ratio at b = 3: PROVED for K* ≤ 3 (open only at K* ≥ 4; largest ratio seen there: 5/4)
SSP mid-term — 6
Notes: Two levels: exact formula at K*=3 (the common case for positive gaps), and unconditional bounds for every K*. R is the optimal number of re-insertions (tools that leave and come back). The counting law floor((2b-q)/3) comes from a two-line double-counting argument over the three configurations. Emphasise "tight at every known extremum": 6-ring, the b=4 witness, and the b=5 witnesses all attain it exactly — these laws look like the true worst case, which is the open question we now pose.

## Slide 7
We refuted our own conjecture
The natural law “gap ≤ K* − 2” is FALSE — with a certificate
Counterexample (b = 5, nine tools, K* = 3):
T = ({0,1,2,4,7}, {0,4,5}, {1,5}, {2,6,8}, {3,4,5,8})
optimum 4, heuristic 6: gap = 2 > 1 = K*−2, ratio 3/2
verified exhaustively by two independent implementations
Every prior test (≈1,400 instances) used b ≤ 4 — exactly the region where our theorems make the law TRUE. The counterexample sits ON the boundary of the proved regimes and attains our bound with equality.
Why this is a good outcome
The proved regime theorems told the search WHERE to look.
The quantitative laws survive and are tight at the witness — they, not K*−2, are the candidates for the exact worst case.
New open question: is min(q, ⌊(2b−q)/3⌋) − R the exact worst case at K* = 3?
Also settled: the ring pattern “positive gap ⇒ K*=3” fails beyond edge instances; ratio 3/2 occurs already at K*=3.
SSP mid-term — 7
Notes: Tell it as a story: we conjectured gap <= K*-2 from all known data; we proved it on wide regimes; the proofs delimited exactly one corner where it COULD fail (2b >= q+3R+6, so capacity at least 5); a directed search there found two counterexamples in minutes. Science working as intended: the theory aimed the telescope. Both witnesses hit our quantitative bound with equality, which upgrades those bounds from "progress" to "candidate exact law".

## Slide 8
Which structure decides these questions?
Two clean answers — one negative, one positive
The gap: NOT combinatorial
Two instances with IDENTICAL conflict structure (same circuit clutter, same K*, same optimum) have different gaps (0 vs 1).
So no criterion reading only job-compatibility can decide when the heuristic is exact — tool-level overlaps are essential (and our K*=3 formula reads exactly those).
JGP tightness: exactly the right clutter
Blocking duality (the “dual”): clusters of a job ↔ minimal group-covers. On the k-ring the covering LP equals k/2 while K* = ⌈k/2⌉:
tight for even k — gap ½ for every odd k
Odd circular structure is the first obstruction family for the set-covering relaxation behind JGP branch-and-price — the exact parallel of odd holes in perfection theory. (Verified k = 5…9; two-line dual proof.)
SSP mid-term — 8
Notes: Left: the impossibility result — even knowing the complete "which job sets fit together" structure cannot predict the gap. Right: the Wagler thread. Blocker = the dual clutter (minimal transversals). For JGP the pair is clusters vs covers, and the ring computes by hand: weight one-half on each adjacent pair. Odd rings give the first provable integrality gap of the JGP covering LP — the relaxation that makes JGP branch-and-price fast. Question we bring to Prof. Wagler: is odd-ring structure THE obstruction (a Lehman/idealness characterisation)?

## Slide 9
The benchmark campaign
Every exact method, one canonical metric, honest protocol
Methods
8 Benders configs (our BBC, full ablation) + LSS ’04 + Catanzaro F4 ’15 + SSPMF ’24 + our branch-and-price (PCF′, PTF)
Instances
1,421 standard files (Catanzaro, Crama, Laporte) — n up to 40, tools up to 60
Protocol
3600 s / 600 s limits · pinned threads · early-stop after 8 straight failures · every solver’s answer re-scored by one KTNS metric (obj_ktns)
Integrity
806 instances solved by someone; ZERO disagreements between any two methods
SSP mid-term — 9
Notes: Points to make: (1) we re-run the literature baselines ourselves on the same hardware, same solver generation — cross-paper wall-clock comparisons are meaningless; (2) one canonical metric: whatever a solver reports, we re-evaluate its returned sequence with KTNS, so conventions cannot distort the comparison; (3) early-stop: a method that fails 8 increasingly-hard instances in a row abandons the rest, so weak methods do not burn weeks; (4) the integrity line: not a single optimality disagreement anywhere.

## Slide 10
Results: who solves what
Instances solved to proven optimality
Chart: 
| SSPMF (primary only) | LSS 2004 | Catanzaro F4 | best Benders (BBC-LP) | PCF′ B&P (n≤25) | PTF B&P (n≤25)
solved | 138 | 759 | 546 | 27 | 94 | 72
SSPMF strongest on primary — the 2024 SOTA claim replicates in our hands.
The 2004 formulation, modern solver: matches 2015 and dominates the secondary suite.
Everyone’s wall: n = 15 with 30+ tools; nobody solves n ≥ 30.
SSP mid-term — 10
Notes: Numbers: SSPMF 138/165 attempted on primary; LSS 759 total (91 primary + 668 secondary of 678 attempted); CATZ 546; our Benders best config 27; branch-and-price 94 and 72 on its validated range n<=25, none at n>=30. Two honest messages: da Silva’s state-of-the-art claim replicates; and solver generation matters more than 2004-vs-2015 formulation differences — a benchmarking-hygiene point the community should hear.

## Slide 11
The diagnosis
Why our Benders stalls — and the number that rules everything
Chart: seconds
| 0 | 600 | 1200 | 1800 | 2400 | 3000 | 3600
incumbent (best found) | 10 | 10 | 10 | 10 | 10 | 10 | 10
proof (dual bound) | 2 | 2 | 2 | 2 | 2 | 2 | 2
A frozen proof: optimum found in seconds, dual bound stuck at the trivial root value for the full hour (250k nodes, 75k cuts). Fractional cuts: structurally inactive — zero violated cuts exist.
Chart: 
| bound = optimum (easy regime) | bound < optimum (hard regime)
tightness | 47.9 | 52.1
47.9% of solved benchmark instances have optimum = |U|−b. The suite splits in half — the easy half is where all methods (and the heuristic) win; the hard half is where new mathematics is needed.
SSP mid-term — 11
Notes: Left: the mechanism, honestly. Our Benders master knows only pairwise information; on capacity-loose instances that is zero, so the proof side never moves — a structural limit, not a bug (we verified the cut machinery is correct and even fixed and re-tested the fractional-cut path; no violated fractional cut exists for this master). The one-line theory fix — putting the coverage bound into the master — is implemented and queued as the next experiment. Right: the unifying statistic. This 48/52 split IS the report’s thesis made empirical.

## Slide 12
Where this goes next
Phases fixed by dependency — and what we ask of you
Now
Master-LP fix for Benders (coverage row) — the fair re-test
queued
Next
Exact worst-case law at K*=3: is our bound the truth? Directed search + proof attempts on the boundary regimes
theory
With Prof. Wagler
PTF polytope: facets on the known witnesses (PORTA), odd-ring idealness question for JGP
polyhedral
Writing
One paper: the worst-case theory + the bound-limited diagnosis (empirical half already in the report)
paper
Questions for this meeting: (1) is the theory-led single-paper packaging right? (2) which side of the blocking pair did Prof. Wagler intend — clusters/covers or circuits/groups? (3) priority between the Benders re-test and the polytope study?
SSP mid-term — 12
Notes: Close with ownership of the plan and three concrete questions. If asked about timing: computational work is effectively done except the one queued re-test; the remaining risk is theory time, which the paper does not depend on (conjectures carry no load — everything in the report is proved or labelled).